## Slide 1: chapter 2
The Computer

## Slide 2: The Computer
a computer system is made up of various elements
each of these elements affects the interaction
  input devices – text entry and pointing
  output devices – screen (small&large), digital paper
  virtual reality – special interaction and display devices
  physical interaction – e.g. sound, haptic, bio-sensing
  memory – RAM & permanent media, capacity & access
  processing – speed of processing, networks

## Slide 3: A ‘typical’ computer system
screen, or monitor, on which there are windows
keyboard
mouse/trackpad
variations
  desktop
  laptop
  PDA
the devices dictate the styles of interaction that the system supports
If we use different devices, then the interface will support a different style of interaction

## Slide 4: How many computers …
in your house?
  PC
  TV, VCR, DVD, HiFi, cable/satellite TV
  microwave, cooker, washing machine
  central heating
  security system
  can you think of more?
in your pockets?
  PDA
  phone, camera
  smart card, card with magnetic strip?
  electronic car key
  USB memory
  try your pockets and bags

## Slide 5: Interactivity?
Long ago … batch processing
  punched card stacks or large data files prepared
  long wait ….
  line printer output
  … and if it is not right …
Now most computing is interactive
  rapid feedback
  the user in control (most of the time)
  doing rather than thinking …
Is faster always better?

## Slide 6: Richer interaction
sensors
and devices
everywhere

## Slide 7: text entry devices
keyboards (QWERTY et al.)
chord keyboards, phone pads
handwriting, speech

## Slide 8: Keyboards
Most common text input device
Allows rapid entry of text by experienced users
Keypress closes connection, causing a character code to be sent
Usually connected by cable, but can be wireless

## Slide 9: layout – QWERTY
Standardised layout
but …
  non-alphanumeric keys are placed differently
  accented symbols needed for different scripts
  minor differences between UK and USA keyboards
QWERTY arrangement not optimal for typing – layout to prevent typewriters jamming!
Alternative designs allow faster typing but large social base of QWERTY typists produces reluctance to change.

## Slide 10: QWERTY (ctd)

## Slide 11: alternative keyboard layouts
Alphabetic
  keys arranged in alphabetic order
  not faster for trained typists
  not faster for beginners either!
Dvorak
  common letters under dominant fingers
  biased towards right hand
  common combinations of letters alternate between hands
  10-15% improvement in speed and reduction in fatigue
  But - large social base of QWERTY typists produce market pressures not to change

## Slide 12: special keyboards
designs to reduce fatigue for RSI
for one handed use
  e.g. the Maltron left-handed keyboard

## Slide 13: Chord keyboards
only a few keys - four or 5
letters typed as combination of keypresses
compact size
– ideal for portable applications
short learning time – keypresses reflect letter shape
fast
– once you have trained
BUT - social resistance, plus fatigue after extended use
NEW – niche market for some wearables

## Slide 14: phone pad and T9 entry
use numeric keys with multiple presses
  2 – a b c 6 - m n o
  3 - d e f 7 - p q r s
  4 - g h i 8 - t u v
  5 - j k l 9 - w x y z
hello = 4433555[pause]555666
surprisingly fast!
T9 predictive entry
  type as if single key for each letter
  use dictionary to ‘guess’ the right word
  hello = 43556 …
  but 26 -> menu ‘am’ or ‘an’

## Slide 15: Handwriting recognition
Text can be input into the computer, using a pen and a digesting tablet
  natural interaction
Technical problems:
  capturing all useful information - stroke path, pressure, etc. in a natural manner
  segmenting joined up writing into individual letters
  interpreting individual letters
  coping with different styles of handwriting
Used in PDAs, and tablet computers … … leave the keyboard on the desk!

## Slide 16: Speech recognition
Improving rapidly
Most successful when:
  single user – initial training and learns peculiarities
  limited vocabulary systems
Problems with
  external noise interfering
  imprecision of pronunciation
  large vocabularies
  different speakers

## Slide 17: Numeric keypads
for entering numbers quickly:
  calculator, PC keyboard
for telephones
not the same!!
ATM like phone
4
5
6
7
8
9
*
0
#
1
2
3
4
5
6
1
2
3
0
.
=
7
8
9
telephone
calculator

## Slide 18: positioning, pointing and drawing
mouse, touchpad trackballs, joysticks etc. touch screens, tablets eyegaze, cursors

## Slide 19: the Mouse
Handheld pointing device
  very common
  easy to use
Two characteristics
  planar movement
  buttons
    (usually from 1 to 3 buttons on top, used for making a selection, indicating an option, or to initiate drawing etc.)

## Slide 20: the mouse (ctd)
Mouse located on desktop
  requires physical space
  no arm fatigue
Relative movement only is detectable.
Movement of mouse moves screen cursor
Screen cursor oriented in (x, y) plane, mouse movement in (x, z) plane …
… an indirect manipulation device.
  device itself doesn’t obscure screen, is accurate and fast.
  hand-eye coordination problems for novice users

## Slide 21: How does it work?
Two methods for detecting motion
Mechanical
  Ball on underside of mouse turns as mouse is moved
  Rotates orthogonal potentiometers
  Can be used on almost any flat surface
Optical
  light emitting diode on underside of mouse
  may use special grid-like pad or just on desk
  less susceptible to dust and dirt
  detects fluctuating alterations in reflected light intensity to calculate relative motion in (x, z) plane

## Slide 22: Even by foot …
some experiments with the footmouse
  controlling mouse movement with feet …
  not very common :-)
but foot controls are common elsewhere:
  car pedals
  sewing machine speed control
  organ and piano pedals

## Slide 23: Touchpad
small touch sensitive tablets
‘stroke’ to move mouse pointer
used mainly in laptop computers
good ‘acceleration’ settings important
  fast stroke
    lots of pixels per inch moved
    initial movement to the target
  slow stroke
    less pixels per inch
    for accurate positioning

## Slide 24: Trackball and thumbwheels
Trackball
  ball is rotated inside static housing
    like an upsdie down mouse!
  relative motion moves cursor
  indirect device, fairly accurate
  separate buttons for picking
  very fast for gaming
  used in some portable and notebook computers.
Thumbwheels …
  for accurate CAD – two dials for X-Y cursor position
  for fast scrolling – single dial on mouse

## Slide 25: Joystick and keyboard nipple
Joystick
  indirect pressure of stick = velocity of movement
  buttons for selection on top or on front like a trigger
  often used for computer games aircraft controls and 3D navigation
Keyboard nipple
  for laptop computers
  miniature joystick in the middle of the keyboard

## Slide 26: Touch-sensitive screen
Detect the presence of finger or stylus on the screen.
  works by interrupting matrix of light beams, capacitance changes or ultrasonic reflections
  direct pointing device
Advantages:
  fast, and requires no specialised pointer
  good for menu selection
  suitable for use in hostile environment: clean and safe from damage.
Disadvantages:
  finger can mark screen
  imprecise (finger is a fairly blunt instrument!)
    difficult to select small regions or perform accurate drawing
  lifting arm can be tiring

## Slide 27: Stylus and light pen
Stylus
  small pen-like pointer to draw directly on screen
  may use touch sensitive surface or magnetic detection
  used in PDA, tablets PCs and drawing tables
Light Pen
  now rarely used
  uses light from screen to detect location
BOTH …
  very direct and obvious to use
  but can obscure screen

## Slide 28: Digitizing tablet
Mouse like-device with cross hairs
used on special surface - rather like stylus
very accurate - used for digitizing maps

## Slide 29: Eyegaze
control interface by eye gaze direction
  e.g. look at a menu item to select it
uses laser beam reflected off retina
  … a very low power laser!
mainly used for evaluation
potential for hands-free control
high accuracy requires headset
cheaper and lower accuracy devices available sit under the screen like a small webcam

## Slide 30: Cursor keys
Four keys (up, down, left, right) on keyboard.
Very, very cheap, but slow.
Useful for not much more than basic motion for text-editing tasks.
No standardised layout, but inverted “T”, most common

## Slide 31: Discrete positioning controls
in phones, TV controls etc.
  cursor pads or mini-joysticks
  discrete left-right, up-down
  mainly for menu selection

## Slide 32: display devices
bitmap screens (CRT & LCD)
large & situated displays digital paper

## Slide 33: bitmap displays
screen is vast number of coloured dots

## Slide 34: resolution and colour depth
Resolution … used (inconsistently) for
  number of pixels on screen (width x height)
    e.g. SVGA 1024 x 768, PDA perhaps 240x400
  density of pixels (in pixels or dots per inch - dpi)
    typically between 72 and 96 dpi
Aspect ratio
  ration between width and height
  4:3 for most screens, 16:9 for wide-screen TV
Colour depth:
  how many different colours for each pixel?
  black/white or greys only
  256 from a pallete
  8 bits each for red/green/blue = millions of colours

## Slide 35: anti-aliasing
Jaggies
  diagonal lines that have discontinuities in due to horizontal raster scan process.
Anti-aliasing
  softens edges by using shades of line colour
  also used for text

## Slide 36: Cathode ray tube
Stream of electrons emitted from electron gun, focused and directed by magnetic fields, hit phosphor-coated screen which glows
used in TVs and computer monitors

## Slide 37: Health hazards of CRT !
X-rays: largely absorbed by screen (but not at rear!)
UV- and IR-radiation from phosphors: insignificant levels
Radio frequency emissions, plus ultrasound (~16kHz)
Electrostatic field - leaks out through tube to user. Intensity dependant on distance and humidity. Can cause rashes.
Electromagnetic fields (50Hz-0.5MHz). Create induction currents in conductive materials, including the human body. Two types of effects attributed to this: visual system - high incidence of cataracts in VDU operators, and concern over reproductive disorders (miscarriages and birth defects).

## Slide 38: Health hints …
do not sit too close to the screen
do not use very small fonts
do not look at the screen for long periods without a break
do not place the screen directly in front of a bright window
work in well-lit surroundings
Take extra care if pregnant. but also posture, ergonomics, stress

## Slide 39: Liquid crystal displays
Smaller, lighter, and … no radiation problems.
Found on PDAs, portables and notebooks, … and increasingly on desktop and even for home TV
also used in dedicted displays: digital watches, mobile phones, HiFi controls
How it works …
  Top plate transparent and polarised, bottom plate reflecting.
  Light passes through top plate and crystal, and reflects back to eye.
  Voltage applied to crystal changes polarisation and hence colour
  N.B. light reflected not emitted => less eye strain

## Slide 40: special displays
Random Scan (Directed-beam refresh, vector display)
  draw the lines to be displayed directly
  no jaggies
  lines need to be constantly redrawn
  rarely used except in special instruments
Direct view storage tube (DVST)
  Similar to random scan but persistent => no flicker
  Can be incrementally updated but not selectively erased
  Used in analogue storage oscilloscopes

## Slide 41: large displays
used for meetings, lectures, etc.
technology
  plasma – usually wide screen
  video walls – lots of small screens together
  projected – RGB lights or LCD projector
    hand/body obscures screen
    may be solved by 2 projectors + clever software
  back-projected
    frosted glass + projector behind

## Slide 42: situated displays
displays in ‘public’ places
  large or small
  very public or for small group
display only
  for information relevant to location
or interactive
  use stylus, touch sensitive screem
in all cases … the location matters
  meaning of information or interaction is related to the location

## Slide 43: virtual reality and 3D interaction
positioning in 3D space moving and grasping
seeing 3D (helmets and caves)

## Slide 44: positioning in 3D space
cockpit and virtual controls
  steering wheels, knobs and dials … just like real!
the 3D mouse
  six-degrees of movement: x, y, z + roll, pitch, yaw
data glove
  fibre optics used to detect finger position
Virtual Reality helmets
  detect head motion and possibly eye gaze
whole body tracking
  accelerometers strapped to limbs or reflective dots and video processing

## Slide 45: 3D displays
desktop VR
  ordinary screen, mouse or keyboard control
  perspective and motion give 3D effect
seeing in 3D
  use stereoscopic vision
  VR helmets
  screen plus shuttered specs, etc.
also see extra slides on 3D vision

## Slide 46: VR headsets
small TV screen for each eye
slightly different angles
3D effect

## Slide 47: VR motion sickness
time delay
  move head … lag … display moves
  conflict: head movement vs. eyes
depth perception
  headset gives different stereo distance
  but all focused in same plane
  conflict: eye angle vs. focus
conflicting cues => sickness
  helps motivate improvements in technology

## Slide 48: simulators and VR caves
scenes projected on walls
realistic environment
hydraulic rams!
real controls
other people

## Slide 49: physical controls, sensors etc.
special displays and gauges
sound, touch, feel, smell
physical controls
environmental and bio-sensing

## Slide 50: dedicated displays
analogue representations:
  dials, gauges, lights, etc.
digital displays:
  small LCD screens, LED lights, etc.
head-up displays
  found in aircraft cockpits
  show most important controls … depending on context

## Slide 51: Sounds
beeps, bongs, clonks, whistles and whirrs
used for error indications
confirmation of actions e.g. Keyclick

## Slide 52: Touch, feel, smell
touch and feeling important
  in games … vibration, force feedback
  in simulation … feel of surgical instruments
  called haptic devices
texture, smell, taste
  current technology very limited

## Slide 53: physical controls
specialist controls needed …
  industrial controls, consumer products, etc.
large buttons
clear dials
tiny buttons
multi-function control
easy-clean
smooth buttons

## Slide 54: Environment and bio-sensing
sensors all around us
  car courtesy light – small switch on door
  ultrasound detectors – security, washbasins
  RFID security tags in shops
  temperature, weight, location
… and even our own bodies …
  iris scanners, body temperature, heart rate, galvanic skin response, blink rate

## Slide 55: paper: printing and scanning
print technology
fonts, page description, WYSIWYG
scanning, OCR

## Slide 56: Printing
image made from small dots
  allows any character set or graphic to be printed,
critical features:
  resolution
    size and spacing of the dots
    measured in dots per inch (dpi)
  speed
    usually measured in pages per minute
  cost!!

## Slide 57: Types of dot-based printers
dot-matrix printers
  use inked ribbon (like a typewriter
  line of pins that can strike the ribbon, dotting the paper.
  typical resolution 80-120 dpi
ink-jet and bubble-jet printers
  tiny blobs of ink sent from print head to paper
  typically 300 dpi or better .
laser printer
  like photocopier: dots of electrostatic charge deposited on drum, which picks up toner (black powder form of ink) rolled onto paper which is then fixed with heat
  typically 600 dpi or better.

## Slide 58: Printing in the workplace
shop tills
  dot matrix
  same print head used for several paper rolls
  may also print cheques
thermal printers
  special heat-sensitive paper
  paper heated by pins makes a dot
  poor quality, but simple & low maintenance
  used in some fax machines

## Slide 59: Fonts
Font – the particular style of text
Courier font
Helvetica font
Palatino font
Times Roman font
§´µº¿Â Ä¿~ (special symbol)
Size of a font measured in points (1 pt about 1/72”) (vaguely) related to its height
This is ten point Helvetica
This is twelve point
This is fourteen point
This is eighteen point
and this is twenty-four point

## Slide 60: Fonts (ctd)
Pitch
  fixed-pitch – every character has the same width
    e.g. Courier
  variable-pitched – some characters wider
    e.g. Times Roman – compare the ‘i’ and the “m”
Serif or Sans-serif
  sans-serif – square-ended strokes
    e.g. Helvetica
  serif – with splayed ends (such as)
    e.g. Times Roman or Palatino

## Slide 61: Readability of text
lowercase
  easy to read shape of words
UPPERCASE
  better for individual letters and non-words e.g. flight numbers: BA793 vs. ba793
serif fonts
  helps your eye on long lines of printed text
  but sans serif often better on screen

## Slide 62: Page Description Languages
Pages very complex
  different fonts, bitmaps, lines, digitised photos, etc.
Can convert it all into a bitmap and send to the printer … but often huge !
Alternatively Use a page description language
  sends a description of the page can be sent,
  instructions for curves, lines, text in different styles, etc.
  like a programming language for printing!
PostScript is the most common

## Slide 63: Screen and page
WYSIWYG
  what you see is what you get
  aim of word processing, etc.
but …
  screen: 72 dpi, landscape image
  print: 600+ dpi, portrait
can try to make them similar but never quite the same
so … need different designs, graphics etc, for screen and print

## Slide 64: Scanners
Take paper and convert it into a bitmap
Two sorts of scanner
  flat-bed: paper placed on a glass plate, whole page converted into bitmap
  hand-held: scanner passed over paper, digitising strip typically 3-4” wide
Shines light at paper and note intensity of reflection
  colour or greyscale
Typical resolutions from 600–2400 dpi

## Slide 65: Scanners (cntd)
Used in
  desktop publishing for incorporating photographs and other images
  document storage and retrieval systems, doing away with paper storage
  special scanners for slides and photographic negatives

## Slide 66: Optical character recognition
OCR converts bitmap back into text
different fonts
  create problems for simple “template matching” algorithms
  more complex systems segment text, decompose it into lines and arcs, and decipher characters that way
page format
  columns, pictures, headers and footers

## Slide 67: Paper-based interaction
paper usually regarded as output only
can be input too – OCR, scanning, etc.
Xerox PaperWorks
  glyphs – small patterns of /\\//\\\
    used to identify forms etc.
    used with scanner and fax to control applications
more recently
  papers micro printed - like wattermarks
    identify which sheet and where you are
  special ‘pen’ can read locations
    know where they are writing

## Slide 68: memory
short term and long term
speed, capacity, compression
formats, access

## Slide 69: Short-term Memory - RAM
Random access memory (RAM)
  on silicon chips
  100 nano-second access time
  usually volatile (lose information if power turned off)
  data transferred at around 100 Mbytes/sec
Some non-volatile RAM used to store basic set-up information
Typical desktop computers: 64 to 256 Mbytes RAM

## Slide 70: Long-term Memory - disks
magnetic disks
  floppy disks store around 1.4 Mbytes
  hard disks typically 40 Gbytes to 100s of Gbytes access time ~10ms, transfer rate 100kbytes/s
optical disks
  use lasers to read and sometimes write
  more robust that magnetic media
  CD-ROM - same technology as home audio, ~ 600 Gbytes
  DVD - for AV applications, or very large files

## Slide 71: Blurring boundaries
PDAs
  often use RAM for their main memory
Flash-Memory
  used in PDAs, cameras etc.
  silicon based but persistent
  plug-in USB devices for data transfer

## Slide 72: virtual memory
Problem:
  running lots of programs + each program large
  not enough RAM
Solution - Virtual memory :
  store some programs temporarily on disk
  makes RAM appear bigger
But … swopping
  program on disk needs to run again
  copied from disk to RAM
  s l o w s t h i n g s d o w n

## Slide 73: Compression
reduce amount of storage required
lossless
  recover exact text or image – e.g. GIF, ZIP
  look for commonalities:
    text: AAAAAAAAAABBBBBCCCCCCCC 10A5B8C
    video: compare successive frames and store change
lossy
  recover something like original – e.g. JPEG, MP3
  exploit perception
    JPEG: lose rapid changes and some colour
    MP3: reduce accuracy of drowned out notes

## Slide 74: Storage formats - text
ASCII - 7-bit binary code for to each letter and character
UTF-8 - 8-bit encoding of 16 bit character set
RTF (rich text format) - text plus formatting and layout information
SGML (standardized generalised markup language) - documents regarded as structured objects
XML (extended markup language) - simpler version of SGML for web applications

## Slide 75: Storage formats - media
Images:
  many storage formats : (PostScript, GIFF, JPEG, TIFF, PICT, etc.)
  plus different compression techniques (to reduce their storage requirements)
Audio/Video
  again lots of formats : (QuickTime, MPEG, WAV, etc.)
  compression even more important
  also ‘streaming’ formats for network delivery

## Slide 76: methods of access
large information store
  long time to search => use index
  what you index -> what you can access
simple index needs exact match
forgiving systems:
  Xerox “do what I mean” (DWIM)
  SOUNDEX – McCloud ~ MacCleod
access without structure …
  free text indexing (all the words in a document)
  needs lots of space!!

## Slide 77: processing and networks
finite speed (but also Moore’s law)
limits of interaction
networked computing

## Slide 78: Finite processing speed
Designers tend to assume fast processors, and make interfaces more and more complicated
But problems occur, because processing cannot keep up with all the tasks it needs to do
  cursor overshooting because system has buffered keypresses
  icon wars - user clicks on icon, nothing happens, clicks on another, then system responds and windows fly everywhere
Also problems if system is too fast - e.g. help screens may scroll through text much too rapidly to be read

## Slide 79: Moore’s law
computers get faster and faster!
1965 …
  Gordon Moore, co-founder of Intel, noticed a pattern
  processor speed doubles every 18 months
  PC … 1987: 1.5 Mhz, 2002: 1.5 GHz
similar pattern for memory
  but doubles every 12 months!!
  hard disk … 1991: 20Mbyte : 2002: 30 Gbyte
baby born today
  record all sound and vision
  by 70 all life’s memories stored in a grain of dust!

## Slide 80: Limitations on interactive performance
Computation bound
  Computation takes ages, causing frustration for the user
Storage channel bound
  Bottleneck in transference of data from disk to memory
Graphics bound
  Common bottleneck: updating displays requires a lot of effort - sometimes helped by adding a graphics co-processor optimised to take on the burden
Network capacity
  Many computers networked - shared resources and files, access to printers etc. - but interactive performance can be reduced by slow network speed

## Slide 81: Networked computing
Networks allow access to …
  large memory and processing
  other people (groupware, email)
  shared resources – esp. the web
Issues
  network delays – slow feedback
  conflicts - many people update data
  unpredictability